## Slide 1: Design and Implementation of a low-cost, open source IoT system using ESP32 with OLED, ThingsBoard and MQTT protocol
Jeong Hoon Choi
USCID: 5023184813
DSCI-560
Data Science Professional Practicum

## Slide 2: Introduction
Interconnection of Renewable generation sources to generate and supply energy presents numerous challenges.
Diverse sensors, micro-controllers, micro-processor (MCU), actuators, valves, pumps, etc.
Supervisory Control and Data Acquisition (SCADA): telemetry and data acquisition
Data acquisition, Data presentation, Supervisory control, Networked data communication, Alarm processing, Historic data storage, data trending and reporting, and Remote monitoring.

## Slide 3: Overview of Technologies
Internet of Things (IoT)
Three/Five-layer architectures
MQTT(Application) – TCP (Transport Layer) – IPv4 (Internet Layer) – IEEE 802.11 (Network Access Layer)
Message Queuing Telemetry Transport (MQTT) Protocol
2 bytes fixed header -> low bandwidths, low computational power, low memory, low battery usage.
Broker can serve several Subscribers and Publisher
Quality of Service: three levels, reliable and suitable for IoT applications

## Slide 4: SCADA System Components
Sensors: MH Electronic Voltage Sensor modules (voltage sensor), ACS 712 Hall Effect Current Sensor (current sensor)
TTGO ESP32 LoRa32 OLED micro-controller (RTU): MQTT Client, measure real-time PV voltage and current values, display OLED, publishes to MQTT broker
Raspberry Pi single-board Computer: ThingsBoard IoT server (MQTT Broker)
Wi-Fi Router (TCP/IP Wi-Fi connection): wireless connection between MQTT Client (ESP32) to MQTT Broker (Raspberry Pi)
ThingsBoard local server IoT platform: Data collection, processing, visualization, and device management

## Slide 5
Question:
I learned the importance of power in IoT. According to the paper, wireless routers consume a significant portion of total power. In reality, installing routers in certain IoT environments and establishing network communications can be challenging. What Solutions are available?
Answer:
My research online and through ChatGPT suggests that cellular networks are used to transmit data in remote areas without Wi-Fi. Low power cellular networks like LT-M and NB-IoT can be used to transmit network packets to a hub using base station signals.